## Slide 1: 第十三讲 无线局域网

## Slide 2: 本章内容
无线局域网
MAC子层

## Slide 3: Characteristics of selected wireless links
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)

## Slide 4: 局域网的扩展
无线局域网和有线局域网的应用场景
  有线局域网
    骨干网
    服务器、工作站等通常位于有线局域网
  无线局域网
    大的空旷场所（机场、车站）
    厂房、股票交易所、古迹、仓库

## Slide 5: Elements of a wireless network
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network
network
infrastructure

## Slide 6
无线局域网的配置
  有线网络作为backbone
  控制模块（CM）扮演无线局域网的接入点
  具有交换或者路由的能力
  Hub等用户模块（UM）也是组成部分
  单cell的配置，仅有一个CM
  多cell的配置，多个CM，通过有线网络连接

## Slide 7
单Cell配置

## Slide 8
多Cell配置

## Slide 9
无线局域网的应用
  大楼间互连：使用点对点无线连接两个路由器或者桥接器
  Nomadic接入：移动设备接入网络，笔记本、PDA接入办公或者校园网
  Ad hoc组网：为临时的需求建立临时的网络

## Slide 10: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET

## Slide 11: 对无线局域网的要求
吞吐量
节点数量：数百个
连接骨干局域网
覆盖区域：直径100~300米
电池能量考虑：MAC协议需要考虑节量，例如，频繁地握手或者持续地监测接入点的MAC协议不可取
健壮性和安全性
多个网络覆盖：一个地区应该允许被多个网络覆盖
不涉及频段授权
Cell之间的切换、漫游
动态配置：动态地添加、删除、或者重配置终端系统

## Slide 12
比较三种技术
三种无线局域网
  红外（IR）局域网
  扩频局域网
  窄带微波

## Slide 13: 红外局域网
对比微波的优势
  有无限频段，理论上有无限带宽
  尚未regulated
  设备便宜
  能够被浅色的物体反射
    天花板可以反射整个房间的信号
  不能穿墙
    没有“隔墙有耳”的安全问题
    不同房间不会相互干扰

## Slide 14
红外局域网的缺陷
  大量的各类辐射形成干扰
    阳光、灯光均包含红外波噪声，对信号形成干扰
    需要较大能量发射，但是大功率红外线对眼有害
    有限的传输距离
红外数据传输技术
  有向波束
  全向传输
  散射

## Slide 15
有向红外波束
  用于点对点连接
  传输距离取决于发射信号的能量和对准目标
  对准的红外有向波束可以传输数公里
    足以用于大楼间连接
全向传输
  基站位于所有无线终端的视距内
  基站通常位于天花板
  基站是一个多端口信号中继器
    天花板基站可以在整个房间中广播收到的IR信号
    无线终端的发射天线对准天花板基站
散射
  无线终端的发射天线对准天花板散射基站
  IR信号被基站向所有方向散射，被所有终端接收

## Slide 16
  全向视距传输和散射

## Slide 17: 扩频局域网
多cell的配置
每个cell内，peer-to-peer或者hub
Peer-to-Peer
  介质访问算法，例如CSMA
  适合构造ad hoc网络

## Slide 18
Hub
  连接backbone
  可能包含接入控制（access control）
    例如，802.11 point coordination function
  可能以多端口信号中继器的方式工作
  自动切换（handoff）
    移动终端就近连接Hub，当信号能量弱时切换
  Cell中的移动节点
    和hub点对点通信，或者
    在cell内全向广播

## Slide 19: 窄带微波局域网
使用微波频段传输信号，带宽仅够满足传播信号
授权的窄带微波
  通常使用多cell的配置
  避免干扰
未授权的窄带微波
  使用ISM频段（Industrial, Scientific, and Medical）

## Slide 21
multiple access protocols

## Slide 22: Multiple access links, protocols
two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch, host
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 23: Multiple access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 24: An ideal multiple access protocol
given: broadcast channel of rate R bps
desiderata:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple

## Slide 25: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 26: Channel partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = pkt trans time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have pkt, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 27: Channel partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 28: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 29: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success

## Slide 30: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E

## Slide 31: Slotted ALOHA: efficiency
suppose: N nodes with many frames to send, each transmits in slot with probability p
prob that given node has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
max efficiency: find p* that maximizes Np(1-p)N-1
for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = .37
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
at best: channel
used for useful
transmissions 37%
of time!
!

## Slide 32: Pure (unslotted) ALOHA
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 33: Pure ALOHA efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [t0-1,t0] .
P(no other node transmits in [t0,t0+1]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n
= 1/(2e) = .18
even worse than slotted Aloha!

## Slide 34: CSMA (carrier sense multiple access)
CSMA: listen before transmit:
if channel sensed idle: transmit entire frame
if channel sensed busy, defer transmission
human analogy: don’t interrupt others!

## Slide 35: CSMA scenario

## Slide 36: performance of concerned protocol

## Slide 37: CSMA collisions
collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in determining collision probability
spatial layout of nodes

## Slide 38: CSMA/CD (collision detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength
human analogy: the polite conversationalist

## Slide 39: CSMA/CD (collision detection)
spatial layout of nodes

## Slide 40: Ethernet CSMA/CD algorithm
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  longer backoff interval with more collisions

## Slide 41: CSMA/CD efficiency
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!

## Slide 42: CSMA/CA (collision avoid)

## Slide 43: “Taking turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 44: “Taking turns” MAC protocols
polling:
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data

## Slide 45: “Taking turns” MAC protocols
token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T

## Slide 46: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  bluetooth, FDDI, token ring